## Slide 1: Variations in speech-in-noise thresholds as it relates to central inhibitory function
Michael L. Smith1, Michael L. Lee1, Christi W. Miller1, Yu-Hsiang Wu2, Ruth A. Bentler2, & Kelly L. Tremblay1
1. Department of Speech & Hearing Sciences, University of Washington, Seattle, WA USA
2. Department of Communication Sciences & Disorders, University of Iowa, Iowa City, IA USA
Speech understanding in the presence of background noise is a major issue for individuals with hearing impairment
Aging in addition to hearing loss affect central inhibitory function and could potentially contribute to poor speech in noise (SiN) performance
Cortical alpha (7.5-12.5Hz) activity is an indirect measure of central inhibition and is believed to contribute to a person’s ability toy understand SIN
The relationship between Alpha rhythms and SIN perception have been studied (REF), but less is known about how individual resting state alpha relates to SIN performance
Increased alpha activity is believed to aid in the suppression of background noise, thus allowing the listener to focus on the relevant signal (speech).
Purpose of the present study was to examine if an individual’s inhibitory function, as defined by their resting state alpha activity, would predict signal to noise ratio (SNR) thresholds
background
Participants: Adult bilateral hearing aid users (n = 15), age 59-81 (mean = 68.3)
Mild-moderate hearing loss
All subjects wore hearing aids for at least two years prior to testing
All testing was performed unaided
Baseline resting state activity was recorded in a silent, dark environment
EEG Recording
64 channel Neuroscan system
Online sampling rate of 1000Hz
Alternating 2 minute blocks of time with eyes open/eyes closed
Three blocks per condition
SIN Testing
Speech: presented in sound field, single speaker 0° azimuth, 1m away
Noise:4-talker babble in international languages
English sentences presented -10 to +15 SNR in 5dB steps
Noise held constant at 65dB SPL
Data Analysis Pipeline
Alpha power was calculated using Fieldtrip, a MATLAB based toolbox
Trials were defined as eyes open or eyes closed
Bandpass filtered 0.5-50Hz
Down sampled to 250Hz
Independent Component Analysis (ICA) was used to remove biological artifacts such as eye blinks, eye movements, electrocardiogram (EKG), as well as noisy channels (i.e. 60Hz line noise)
  ICA was conducted over the continuous EEG recording
  Average of 3-5 components removed per subject
objectives
Resting state alpha activity in the eyes open condition varied among hearing aid listeners
4. Conclusions
Conclusion 1
Conclusion 2
Conclusion 3
1. Introduction
3. Results
2. Methods
References
FFT – occipital channels
Time frequency averaged across occipital channels
Topographical representation of alpha band power
Figure 4. Oscillatory alpha band activity estimated at the level of the scalp. Top row of panels represents two subjects during the eyes open condition, and with eyes closed in the bottom row. Notice the subject differences in the eyes open condition, and the similarities during eyes closed.
Decreased SNR thresholds were associated with increased alpha power
Figure 4. SNR-50 thresholds as a function of pure tone average (PTA) and age, respectively. Neither PTA or age was significant (p=0.09,p=0.21) in how they affected SNR-50 thresholds.
Figure 3. Significant associations between SNR thresholds and alpha power during the eyes open condition. Eyes closed alpha power did not significantly effect SNR-50 thresholds. Alpha power was calculated as area under the curve from the FFT power spectrum in the alpha frequency band (7.5-12.5Hz).
Figure 1. ICA artifact removal pipeline. A) Select channels showing raw EEG data bandpass filtered 0.5-50Hz. Note the eye blink artifacts across channels, and a large eye movement at ~103 seconds. B) Topo-maps of three independent components (ICs) and their distinct waveforms: eye blinks, EKG, and eye movements respectively. C) EEG data after removal of the ICs. Note the contrast to the raw waveform.
3. Results Continued
Alpha power was primarily concentrated to occipital areas
Alpha power was greater in the eyes closed condition compared to eyes open
SNR-50 thresholds decreased as a function of alpha power during the eyes open condition, and increased during eyes closed
Audibility and age did not significantly contribute to SNR-50 thresholds
EEG alpha power may be predictive of SNR-50 threshold outcome measures
 | Estimate co-efficient | Standard error | P-value
Alpha power eyes open | -39.7 | 12.6 | 0.008**
Alpha power eyes closed | 19.0 | 6.4 | 0.01*
Table 1. Linear regression model (y=β0+ β1X1+ β2X2) where y=SNR-50 threshold, X1=alpha power eyes open, X2=alpha power eyes closed, and β0 the y intercept.
SNR thresholds significantly associate with alpha power
A. Raw EEG Signal
B. ICA Components Removed
C. Clean EEG Data
Eyes Open
Eyes Closed
Eyes Open
Eyes Closed
Eyes Open
Eyes Closed
Figure 2. Fast Fourier Transform (FFT) for two subjects across occipital channels in both the eyes open and eyes closed condition. I
Figure 3. Time frequency data for two subjects. The top row of panels shows oscillatory activation in the eyes open condition, and the bottom row eyes closed, for each subject respectively. Oscillatory activity is shown with the greatest activation in the alpha band (7.5-12.5Hz).
Funding Sources
NIDCD 5R01DC012769-05
Subject 1
Subject 2
Subject 2
Subject 1